## Slide 1: Small Forwarding Table for Fast Routing Lookups
Author: Mikael Degermark, Andrej Brodnik, Svante Carlsson, Stephen Pink
Publisher: SIGCOMM ‘97
Presenter: Chun-Yu, Li
Date: 2016/07/13

## Slide 2: Introduction
Goal:
  To minimize the number of memory accesses for a lookup operation and the size of the data structure.
Span the binary tree to be complete.
  Each node has either two or no children.
  Nodes with a child must be expanded to have two children.
Notes: Leaf pushing: 把不是leaf的prefix node push到leaf上，prefix的資訊都會存在leaf node上
不影響search結果

## Slide 3: Data Structure
The forwarding table is essentially tree with three levels.
  Level 1 covers the prefix tree down to depth 16.
  Level 2 covers depth from 17 to 24.
  Level 3 covers depth from 25 to 32.

## Slide 4: Data Structure
  Cut through the tree at depth 16.
  Represent each node by a bit-vector (total 216=65536 bits).
one:
Root head: Prefix tree continues below the cut. (bits 6, 12, 13)
Genuine head: A leaf at depth 16 or less. (bits 0, 4, 7, 8, 14, 15)
zero:
A member of a range covered by a leaf at a depth less than 16.
(bits 1, 2, 3, 5, 9, 10, 11)
Bit vector
(total 216 bits)
Notes: 有兩種情況我們會用bitmap的1來表示: Root head, Genuine head

## Slide 5: Data Structure
Head information
  Head information is encoded in 16-bit pointers stored in an array (pointer groups).
  Genuine head
    Store an index into the next-hop table.
  Root head:
    Store an index to the level two that represents the corresponding sub-tree.

## Slide 6
2-bit case
  Possible case
  Impossible case
    00、01
1 0
1 1
4-bit case
1 0 0 0
1 0 1 0
1 0 1 1
1 1 1 0
1 1 1 1 Total: 5 cases
Let a(n) be the number of possible non-zero bit-masks of length 2n:
a(n) = 1 + a(n-1)2
Bit mask: 10、11
Bit mask
Notes: Possibly

## Slide 7
8-bit case
16-bit case
1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1
1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 0
.
.
.
Total: 677 cases
1 0 0 0 0 0 0 0
1 0 1 0 1 0 1 0
1 0 1 0 1 0 1 1
1 0 1 0 1 1 1 0
1 0 1 0 1 1 1 1
1 0 1 1 1 0 1 0
.
.
.
Total: 26 cases
Let a(n) be the number of possible non-zero bit-masks of length 2n:
a(n) = 1 + a(n-1)2
Bit mask
Bit mask

## Slide 8: Data Structure
Find the pointer groups
  Code word array & Base index array
The code words contains a 10-bit value(r1, r2,…) and a 6-bit offset (0, 3, 10, …).
After four code words, the offset value might be too large to represent with 6-bit. Use a base index be the offset to find a group of pointers. ( Length of base index array element is 16 bits. )
Bit mask:
=4096
=1024

## Slide 9: Data structure
Maptable

## Slide 10: Search
Search the first level of the data structure.
To find the correct pointer in the group of pointers.
Steps to search 1st level:

## Slide 11: Level 2 & 3
Levels two and three consist of chunks.
Chunks: covers a sub-tree of height 8 and can contain at most 28=256 heads.
  1-8 heads: chunk is “sparse”
    array of 8-bit indices of the heads
  9-64 heads: chunk is “dense”
    just one base index for all 16 codewords
  65-256 heads: chunk is “very dense”
    chunks are searched analogously with the 1st level.