## Slide 1: Reference Router on NetFPGA 1G
Course: | High-Performance Router Architecture and Design
Presenter: | Chun-Yu, Li
Date: | 106/5/16

## Slide 2: INTRODUCTION
Open-source Hardware & Software
  NetFPGA is a platform that, combined with an open source code base (both software and hardware), enable rapid prototyping of networking devices.
Reference Designs
  The reference design for various application can be downloaded from [1], it contains a NIC or an IPv4 Router, even an OpenFlow switch.
For more details (datasheet specs, resources), please refer to [2]. It’s official website for NetFPGA family of boards.

## Slide 3: INTRODUCTION
Reference Router Features [3]
  Forwards IPv4 packets of length 64-1500 bytes.
  Performs Longest Prefix Matching on destination address.
  Allows host receive packets by filter on destination address.
  Generates ICMP message for packets with TTL <= 1.
  Drops packets with bad IP checksum.

## Slide 4: INTRODUCTION
Processing in Reference Router
1. Accept packet arriving on an incoming link.
2. Lookup packet destination address in the forwarding
table to identify outgoing port(s).
3. Manipulate IP header: e.g., decrement TTL, update
header checksum.
4. Buffer packet in the output queue.
5. Transmit packet onto outgoing link.

## Slide 5: NetFPGA 1G BORAD
The NetFPGA 1G is a PCI card that includes the Logic Fabric, Memory, and Gigabit Ethernet Interfaces.
PCI Bus
CPU
Memory
FPGA
1G port
Memory
1G port
1G port
1G port
Host PC
NetFPGA 1G

## Slide 6: NetFPGA 1G BORAD
PHY
PHY
PHY
RGMII
CORE DESIGN
DDR2
SDRAM
DMA
CPCI
SRAM
DDR2
Controller
PHY
PHY
PHY
PHY
Virtex II Pro-50
Notes: MEMORY
PHY
RGMII = Reduced gigabit media-independent interface
DMA
CPCI

## Slide 7: CORE DESIGN
DMA Controller
MDIO Controller
User Data Path
SRAM
Controller
CPCI
Controller
MAC Queues
Register
Group
MAC Queues
MAC Queues
MAC Queue
CPU Queues
CPU Queues
CPU Queues
CPU Queue
Both Rx Queue and Tx Queue
Both Rx Queue and Tx Queue
Receive/Send packet from/to CPU
Allowing CPU write/read register
Communicate with SRAM
Management with PHY

## Slide 8: USER DATA PATH
Input Arbiter
Output Port
Lookup
Output Queues
Register
Master
data
ctrl
wr
rdy
data
ctrl
wr
rdy

## Slide 9: DATA FORMAT
2 bytes | 2 bytes | 2 bytes | 2 bytes |  | 2 bytes |  |  | 
Ctrl Bus | Data Bus |  |  |  |  |  |  | 
0xFF | Destination port | Word length | Source port |  |  | Byte length |  | 
0xXX | Other module header (optional) |  |  |  |  |  |  | 
0x00 | Dst MAC address |  |  |  |  | Src MAC address |  | 
0x00 | Src MAC address |  | Ethertype |  |  | IP ver | Head len | ToS
0x00 | Total length | Identification | Flags | Fragment offset |  | Time to live |  | Protocol
0x00 | Header checksum | Src IP address |  |  |  | Dst IP address |  | 
0x00 | Dst IP address | …… |  |  |  |  |  | 
0x00 | ……. |  |  |  |  |  |  | 
0x00 | …… |  |  |  |  |  |  | 
0x80 | Last byte |  |  |  |  |  |  | 
Prepended metadata
Ethernet Header
IP Header
Protocol Header &
Payload

## Slide 10: OUTPUT PORT LOOKUP
ip_lpm
ip_arp
dest_ip_filter
ip_checksum_ttl
op_lut_hdr_parser
eth_parser
pre_process_ control
op_lut_process_sm
router_op_lut_regs
fallthrough_small_fifo

## Slide 11: OUTPUT PORT LOOKUP
ip_lpm
ip_arp
in_data
next_hop_ip
lpm_output_port
next_hop_ip
lpm_output_port
word_IP_SRC_DST
word_IP_DST_LO
next_hop_mac
output_port
arp_mac_vld
arp_lookup_hit
lpm_lookup_hit
rd_arp_result

## Slide 12: OUTPUT PORT LOOKUP
dst_ip_filter
in_data
word_IP_SRC_DST
word_IP_DST_LO
dst_ip_hit
dst_ip_filter_vld
rd_dst_ip_filter_result

## Slide 13: OUTPUT PORT LOOKUP
ip_checksum_ttl
in_data
word_ETH_IP_VER
word_IP_LEN_ID
ip_checksum_vld
ip_checksum_is_good
rd_checksum
in_wr
word_IP_SRC_DST
word_IP_DST_LO
ip_hdr_has_options
ip_ttl_is_good
ip_new_ttl
ip_new_checksum

## Slide 14: OUTPUT PORT LOOKUP
eth_parser
in_data
word_ETH_IP_VER
word_IP_LEN_ID
is_arp_pkt
is_ip_pkt
eth_parser_rd_info
word_IP_SRC_DST
word_IP_DST_LO
is_for_us
is_broadcast
mac_dst_port_num
eth_parser_info_vld

## Slide 15: OUTPUT PORT LOOKUP
op_lut_hdr_parser
in_data
is_from_cpu
to_cpu_output_port
rd_hdr_parser
from_cpu_output_port
input_port_num
in_ctrl

## Slide 16: FORWARDING DECISION
According to the information from the preprocess blocks, op_lut_process_sm determines the fate of the packet.
Yes
No
Not for us
Not IP
IP
From CPU?
Send to MAC
Dst MAC
Drop
Ether type
Send to CPU

## Slide 17: FORWARDING DECISION
IP checksum correct?
Drop
Send to CPU
Filter table hit?
Send to MAC
No
Yes
Yes
No
Yes
Ver ==4?
No IP opts?
TTL > 1?
Routing table hit?
ARP table hit?
Dec TTL
Update IP checksum
Set Dst MAC
Set Src MAC
IP
No

## Slide 18: EXCEPTION PACKET PATH
Software
Driver
DMA
Registers
HOST
PCI
NetFPGA
User Data Path
CPU
RxQ
CPU
TxQ
CPU
RxQ
CPU
TxQ
Register
Group
CPU
RxQ
CPU
TxQ
CPU
RxQ
CPU
TxQ
MAC
TxQ
MAC
RxQ
MAC
TxQ
MAC
RxQ
MAC
TxQ
MAC
RxQ
MAC
TxQ
MAC
RxQ

## Slide 19: REFERNCE
[1]https://github.com/NetFPGA/netfpga/wiki/Releases
[2]http://netfpga.org/
[3]http://www.cl.cam.ac.uk/research/srg/netos/projects/netfpga/workshop/cambridge-september-2011/2011_NetFPGA_Day_tutorial_Cambridge.pdf