## Slide 1: Hardware accelerator to speed up packet processing in NDN router
Authors: | Weiwen Yu, Derek Pao
Publisher: | 2016 Computer Communication
Presenter: | Tzu-Chieh, Lin
Date: | 106/09/27

## Slide 2: INTRODUCTION
Named Data Networking (NDN) is a new network architecture. Packets under the NDN framework are identified by names , instead of the IP address/port number in the conventional Internet Protocol .
The name in an NDN packet can name anything – an endpoint, a data chunk in a movie or a book.
There are two types of packets in NDN network: Interest packet and Data packet.

## Slide 3: NDN Architectural
Consumer
NDN
Network
Interest Packet
Data Packet

## Slide 5: Name
A video produced by PARC.com may have the name
/parc.com/videos/WidgetA.mpg
Segment 3 of version 1 of the video might be named
/parc.com/videos/WidgetA.mpg/1/3

## Slide 6
Forwarding Information Base

## Slide 7: Packet processing challenges in NDN
A fundamental difference between the packet processing in NDN and conventional TCP/IP routers is that NDN requires stateful processing, whereas TCP/IP only requires stateless processing.
The stateful processing requirement of NDN leads to per-packet update to the PIT and the CS tables.
Hardware should be able to execute update and lookup operations to the PIT/CS tables with the same efficiency.

## Slide 8: Related work
DiPIT and MaPIT are two software-base implementation PIT table using BF(Bloom Filter). Yuan and Crowley present a software implementation of the PIT using d-left hash table.
These software-base implementation can only achieve packet processing rate of a few MPPS (million packets per second).
In this paper, we shall present a hardware accelerator that can improve the packet processing rate of the PIT up to 60 MPPS, and reduce the workload of FIB lookup significantly.

## Slide 9: System Architecture

## Slide 10: nid & sn
Divide the packet name into two logical parts, the content name, and the segment number (sn).
For example, /parc.com/videos/WidgetA.mpg/1/3 have content name /parc.com/videos/WidgetA.mpg/1 and segment number 3.
Variable-length name is converted to a fixed-length 64-bit name ID (nid) using hash function.
hash(/parc.com/… , 3) = 30 , then (nid, sn) = (30, 3)

## Slide 11: PIT & nidT
The software and hardware maintain its own copy of the PIT and nidT.
The hardware table contains only the essential data fields to support the search and update operations.

## Slide 13: Received Interest Packet
NPU
FPGA
 | nid | sn
0x00 | 30 | 0
0x01 | 30 | 1
0x10 | 46 | 0
0x11 | 100 | 5
 | nid | sn | face list | other info
0x00 | 30 | 0 | 0,1 | …
0x01 | 30 | 1 | 0,1 | …
0x10 | 46 | 0 | 2 | …
0x11 | 100 | 5 | 3 | …
LI(30, 0)
(hit, 0x00, ..)

## Slide 14: Received Data Packet
NPU
FPGA
 | nid | sn
0x00 | 30 | 0
0x01 | 30 | 1
0x10 | 46 | 0
0x11 | 100 | 5
 | nid | sn | face list | other info
0x00 | 30 | 0 | 0,1 | …
0x01 | 30 | 1 | 0,1 | …
0x10 | 46 | 0 | 2 | …
0x11 | 100 | 5 | 3 | …
LD(30, 0)
(hit, 0x00, ..)

## Slide 15: Lookup Table